Title : Iptables in Linux Firewall

Intro
Managing network traffic is one of the toughest jobs a system administrators has to deal with. He must configure the firewall in such a way that it will meet the system and users requirements for both incoming and outgoing connections, without leaving the system vulnerable to attacks.
This is where iptables come in handy. Iptables is a Linux command line firewall that allows system administrators to manage incoming and outgoing traffic via a set of configurable table rules.

What is an iptable
Iptables is a command line tool used to set up,and configure the firewall through set of tables to filter packets.
These tables contain multiple chains which are nothing, but the set of rules which can be built-in or user defined according to which the traffic is allowed on the machine. It is one of the way to set-up firewall as iptables monitors the traffic and filter it according to the specified rules.

TABLES
There are currently five independent tables
- filter ==> default table used for filtering packets.
- Nat ==> consulted when a packet that creates a new connection
- mangle ==>used for specialized packet alteration such as alteration ip-headers of the packet
- raw ==> used mainly for configuring exemptions from connection tracking
- security ==>used for Mandatory Access Control (MAC) networking rules

Chains
- point in the route of the packet where we can apply rules
- not all chains available for all tables
- there are 5 types
    • Pre-routing
        ◦ applied to any incomming packet very soon after entering network
        ◦ processed before any routing decision is made
    • Input
        ◦ applied when a packet enteers a system
        ◦ processed after pre-routing
    • Forward
        ◦ applied to a packet that is forwarded through our system
    • Output
        ◦ applied to a packet that is originated from the system or packet going out
    • post-routing
        ◦ applied to a packet that is outgoing or forwarded
        ◦ processed after routing decision is made and just before packet is transmitted
Rules
- they are user defined commands to manipulate the network traffic
- if rules dosent match the next rule in chain is examined
- if rules match then the next rule is specified by rules target value
- rules created are not persistant

Table to show the order in which tables and their respective chains are traversed for validating rules:
Tables/Chains	Pre routing	Input	Forward	Output	Post routing
raw	Y			Y
Mangle	Y	Y	Y	Y	Y
nat(DNAT)	Y			Y
filter		Y	Y	Y
security		Y	Y	Y
nat(SNAT)		Y			Y

Some important chain sequence :
- Incoming packets destined for the local system -> Pre -> Input
- Incoming packets destined for another host-> Pre -> Forward -> Post
- Locally generated packet -> Output -> Post

Example to understand
Lets say we want to block a particular ipaddress, then the following command can be used

 # iptables -A OUTPUT -s ipaddress -j DROP

matching component	target component

-possible matching component
-diff condition available to define rules
-match by protocol type
-destination or source address
-destination or source port
-input or output interface
-headers etc
-can also be combined to create complex rule set

-possible target component
-action triggered when a packet meets a matching criteria
-are of 2 types
-terminating target which ends further traversal
-Accept,drop,queue,reject,return
-non terminating which performs actions and continue the chain
-all actions are not available for every table and chain

Commands with example

Check the status of iptables
# iptables -L -n -v //-L to list rules, -n for numeric format, -v for verbose

Append new rule in a chain
#iptables -t table -A chain -s ipaddress -j DROP
#iptables -t filter -A OUTPUT -s website.com -j DROP //Block specific website

Delete rule no 5 from a chain
#iptables -t table -D chain rule_number
#iptables -t filter -D chain 1	//assuming there is only one rule created

Flushing or deleting IPTables rules
# iptables -F

Making rules persistant
There are 2 ways

iptables-persistent
there is a package with the name "iptables-persistent" which takes over the automatic loading of the saved iptables rules.
 To do this, the rules must be saved in the file /etc/iptables/rules.v4 (for IPv4 )

For use, the package must simply be installed.
apt-get install iptables-persistent
## iptables-save and iptables-restore

$ apsudo sh -c “iptables-save > /etc/iptables.conf” //save the current state of iptables
$ sudo iptables-restore < /etc/iptables.conf //restore from file again

Note :the above command can be added to /etc/rc.local to enable automatic loading of the rules from iptables.conf